Errror:
in line 5 , assign is not used
in line 6 , & operatin is not used between c and (a^b)
Error
in line 18,24,30 a1,b1,c1 are not correctly used.
And in lasr lines end, initial , begin are not used.

(c) Corrected codes
 Listing 4
module full_adder(
 input logic a,
 input logic b,
 input logic c,
 output logic sum,
 output logic carry
 );
 assign sum = (a ^ b) ^ c;
 assign carry = (a & b) | (c&(a ^ b));
endmodule
 Listing 5
module full_adder_tb();
 logic a1;
 logic b1;
 logic c1;
 logic sum1;
 logic carry1;
 full_adder uut(
 .a(a1),
 .b(b1),
 .c(c1),
 .sum(sum1),
 .carry(carry1)
 );
 initial
 begin
 // Provide different combinations of the inputs to check validity of code
 a1 = 0; b1 = 0; c1 = 0;
 #10;
 a1 = 0; b1 = 0; c1 = 1;
 #10;
 a1 = 0; b1 = 1; c1 = 0;
 #10;
 a1 = 0; b1 = 1; c1 = 1;
 #10;
 a1 = 1; b1 = 0; c1 = 0;
 #10;
 a1 = 1; b1 = 0; c1 = 1;
 #10;
 a1 = 1; b1 = 1; c1 = 0;
 #10
 a1 = 1; b1 = 1; c1 = 1;
 #10;
 $stop;
end
 endmodule

https://github.com/abdullahrasheed126/dsd-lab